## Slide 1: Link Layer SECURITY
Summary:
Layer 2 addressing
Layer 2 General Security Issues
Wired L2 Security issues (802.3)
Wireless L2 Security issues (802.11)
Layer 2 protocol recap

## Slide 2: How Layer 2 links work: recap

## Slide 3: Protocol stacks
Application
Transport
Network
Link
Physical
Alice.exe
frame
datagram
segment
message
Bob.exe
application
transport
network
link
physical
AB
12
R2
M
AB
12
M
AB
M
M
network
link
physical
link
physical
AB
12
R2 2
M
AB
12
M
AB
12
1R
M
Router (R)
Switch (S)
Each level has its own packet data unit format (PDU format) M1, M2, MR1, MR2 = MAC addresses I1,I2,IR1,IR2 = IP Addresses PA,PB = Port numbers
2
I1,M1
word.exe …
…excel.exe
ffox.exe …
…emule.exe
M1MR1 | I1I2 | PAPB | M
I1I2 | PAPB | M
PAPB | M
M
I3, M3
AB
12
M
AB
12
1R
M
AB
12
1R
M
IR1, MR1
IR2, MR2

## Slide 4: Embedding – Envelope layers
https://www.wireshark.org/

## Slide 5: Link Layer: Introduction
Some terminology:
hosts and routers are nodes
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs
The layer-2 PDU is a frame, encapsulates datagrams
The data-link layer has responsibility of
transferring datagram from one node
to adjacent node over a link

## Slide 6: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
each link protocol provides different services
  e.g., may or may not provide retransmissions over the link at hand
transportation analogy
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm

## Slide 7: Link Layer Services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, dest
    different from IP address!
reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end2end reliability?

## Slide 8: Where is the link layer implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC)
  Ethernet card, PCMCIA card, 802.11 card
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
host schematic
application
transport
network
link
link
physical

## Slide 9: Adaptors Communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 10: LINK TYPES
Two fundamental types:
Point-to-point (physical or virtual)
  PPP, PPPoA, PPPoE
broadcast (shared medium: space, wires, also virtual)
  Ethernet
  802.11 wireless LAN
  802.1q (Virtual LANs)
Broadcast links are evidently a challenge for confidentiality and integrity
Notes: animazione

## Slide 11: ETHERNET FRAME STRUCTURE
Addresses: 6 bytes
  NICs process incoming frames only if Dst MAC corresponds to the NICs MAC, or to a broadcast address (ff:ff:ff:ff:ff:ff)
  Otherwise a NIC should discard the incoming frame
Type: code of transported layer 3 protocol (e.g. IP, IPv6, IPX and others were and are possible)
CRC: checked by receiver. Frame should be discarded if CRC not corresponding. Not cryptographic. Can be counterfeited.

## Slide 12: MAC Addresses vs IP addresses
IP addresses
  Valid among layer 3 nodes
MAC addresses:
  Work only within current link. Do not need configuration.
  Supposedly “Hardwired” within NICs.
  Cannot be used for authenticating stations. Cannot be used for managing Layer 2 ACLs

## Slide 13
NO

## Slide 14: ARP: Address Resolution Protocol
Any station on a link handles an ARP table
ARP Table: IP/MAC address triples < IP address; MAC address; TTL>
  TTL:
  Time To Live, in msec
Needed when a host must be
reached at layer 2.
Conversion IP -> MAC needed
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
237.196.7.23
237.196.7.78
237.196.7.14
237.196.7.88

## Slide 15: Routing between two LANs
A needs to contact B via R
Assume A knows B’s IP address.
R ha due tabelle ARP, una per dominio di collisione
In routing table at source Host, find router 111.111.111.110
In ARP table at source, find MAC address E6-E9-00-17-BB-4B, etc
A
R
B

## Slide 16
A originates datagram D, A -> B
Is B in the same LAN? NO. Routing is needed via R.
R’s MAC address is needed. ARP is the recipe!
D is embedded in a frame F. Note that F goes from MAC A-> MAC R, but D refers IP A -> IP B
R received F, extracts D, sees B IP, and understands that B is within LAN2
R uses ARP for having the MAC address of B
R creates a frame F2, and sends it to B. F2 contains D (unchanged) but at layer 2 the conversation if between R and B.
B
A
R
Notes: appare datagramma (nel datagramma deve apparire indirizzo mittente e destinatario)
3. appare frame ARP (destinato a tutti). deve comparire mac address mittente: 74-29-ecc-ecc- , destinatario: ff-ff-ff-ff-ff-ff-ff
4.

## Slide 17: General L2 security issues

## Slide 18: ARP Poisoning in LAN

## Slide 19: ARP poisoning in LAN

## Slide 20: Half mitm

## Slide 21: Accidental IP Conflict

## Slide 22: Countermeasures
ARP Watching
Static ARP tables
ARP Jamming
SSL/TLS (but works only on a per app basis)
VPN technologies: IP Sec, Tunnels, SSH
User isolation (a station can talk to the router only)

## Slide 23: DHCP: Dynamic Host Configuration Protocol
goal: host dynamically obtains IP address from network server when it “joins” network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who join/leave network
DHCP overview:
  host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg

## Slide 25: Local to remote attacks (1) DHCP spoofing
The DHCP requests are made in broadcast mode.
If the attacker replies before the real DHCP server it can manipulate:
  IP address of the victim
  GW address assigned to the victim
  DNS address

## Slide 26: Local to remote attacks (1) DHCP spoofing - countermeasures
YES - detection of multiple DHCP replies
YES – dhcp probe
YES – Switch ACLs, DHCP snooping
YES – DHCP starvator

## Slide 27: Reflection attacks with broadcast
Example:
  Fake victim’s IP
  Generate broadcast traffic using the fake IP.
  Answers flood the victim.
  Depending on the type of attack, particular conditions are required
Attacker
Fake IP : 192.168.0.1
Network
Victim
IP: 192.168.0.1
Subnet hosts.
Passive attackers

## Slide 28: COUNTERMEASURES
Limiting ICMP and other types of broadcast on LANs
Configure firewalls
IP spoofings are severely limited from LAN to LAN, but are still possible.
Use Reverse Path Filtering wherever possible

## Slide 29: Other Local MITM Attacks DNS spoofing
HOST
DNS
serverX.localdomain.in
10.1.1.50
MITM
10.1.1.1
If the attacker is able to sniff the ID of the DNS request,
he/she can reply before the real DNS server

## Slide 30: Local attacks DNS spoofing - countermeasures
YES - detect multiple replies (IDS)
YES - use lmhost or hosts file for static resolution of critical hosts
YES – DNSSEC
(not to be confused with DNS over TLS)
host.example.com. 86400 IN RRSIG A 5 3 86400 20030322173103 ( 20030220173103 2642 example.com.
                oJB1W6WNGv+ldvQ3WDG0MQkg5IEhjRip8WTr
                PYGv07h108dUKGMeDPKijVCHX3DDKdfb+v6o
                B9wfuh3DTJXUAfI/M0zmO/zz8bW0Rznl8O3t
                GNazPwQKkRN20XPXV6nwwfoXmJQbsLNrLfkG
                J5D6fwFm8nN+6pBzeDQfsS3Ap3o= )

## Slide 31: MISC: DNS rebinding

## Slide 32: Local to remote attacks (2) ICMP redirect
G1
AT
H
T
LAN
The attacker can forge ICMP redirect packet in order to
redirect traffic to himself
ICMP redirect to AT

## Slide 33: Specific 802.3 (Ethernet) security issues

## Slide 34: Hubs
An hub repeats frames on each ports (expect the incoming one)
doppino intrecciato in rame
hub
Notes: pallino che parte da uno e va verso tutti gli altri

## Slide 35: Switches
When a new frame F enters some interface:
Lookup in the switch table for Dst MAC
if Dst MAC is in switch table then{
if MAC dst.intf = MAC src.intf then ignores this frame
else send F over MAC dst.intf ONLY
}
else broadcast F on all ports (except the incoming one)

## Slide 36: Example
C sends frame F to D
Switch receives F from C
  C is discovered to operate from intf 1. This is recorded.
  It is not known where D operates from
  F is sent to intf 2 and 3
D receives F
hub
hub
hub
switch
A
B
C
D
E
F
G
H
I
address
interface
A
B
E
G
1
1
2
3
1
2
3
Notes: animazione.

## Slide 37: Switch example
When D answers to C:
D answers with F2
  D is discovered to be operating from intf 2. This is recorded
  C is known to work on intf 1, only this interface receives F2
hub
hub
hub
switch
A
B
C
D
E
F
G
H
I
address
interface
A
B
E
G
C
1
1
2
3
1
D 2
Notes: animazione

## Slide 38: Port Stealing: example
C send a frame to R. G is an intruder
G sends frames using R as source MAC. This forces wrong updating of the switch table
G can then capture frames to R, can record, filter and alter them. Then, for avoiding disruption of communication, it sends frames to the real R, stimulating re-update of the switch table
hub
hub
hub
switch
A
B
C
R
G
H
I
address
interface
A
B
R
G
1
1
2
3
1
2
3
Notes: animazione.

## Slide 39: MAC Spoofing / Flooding
Flooding. Idea: the switch table needs memory.
This memory can be saturated producing a huge number of frames with random MAC sources. When this happens, a switch starts behaving like an hub.
Countermeasures: port locking, IEEE 802.1X

## Slide 40: Others under-the-hood protocols
VLAN vulnerabilities (Hopping…)
STP, VSTP…

## Slide 41: Specific 802.11 (Wi-Fi) security issues

## Slide 42: 802.11: the actors
Set of stations (STAs) each with a MAC address, with a radio NIC
Each STA can tune on a channel or hop among channels
AP: STAtions with the role of BSS. Their MAC is the BSSID
An AP group can form a ESS. The ESSID is known as the “Wifi network name”
A STAtion can be associated with a particular BSSID

## Slide 43: NIC Wifi modes
Monitor mode: no filter on the BSSID. All received frames are buffered
Managed mode: only frames where BSSID matches the one the STA is associated to are buffered

## Slide 44: 802.11: BSS & ESS
ESSID = string denoting an AP group. Members of the group should be coordinated.
BSSID = single AP MAC address. Should be unique.
Association: process of entering a virtual collision domain
  Beacon frames
  Probe frames
  Association requests
  Association responses
  Auth requests
  Auth responses

## Slide 45: 802.11 frame: Addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: src MAC address
Address 1: dst MAC address
Address 3: MAC address
BSSID
Address 4: Used in WDS

## Slide 46
Internet
router
AP
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame
802.11 frame: bridging

## Slide 47
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
DS
Subtype
To
DS
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
802.11 frame: more
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for reliable ARQ)
frame type
(RTS, CTS, ACK, data)

## Slide 48: Channel allocation
802.11n APs take two 22Mhz Channel together

## Slide 50: Wifi 802.11 security levels
WLAN open – no security
WLAN closed with WEP
WPA Personal/Enterprise
WPA2 Personal/Enterprise
WPA3 Personal/Enterprise

## Slide 51: WLAN open
Virtually equivalent to an hubbed LAN
Sniffing is possible, but also ESSID & BSSID spoofing is very easy
Issues with captive portals
De-authentication attacks can block traffic
  Primitive solution: WEP

## Slide 52: Rogue ESSIDs
Technique:
  Spoof ESSIDs, force association to wrong BSSID
  Can MITM a whole set of stations
  Results depend on the security level of victim ESSID

## Slide 54: Captive portals
A dirty workaround for
controlling network access
Breaks many standard protocols
and is not HTTPS friendly

## Slide 55: WLAN WEP
Very simple cryptography with pre-shared key
Each frame is encoded in terms of
  RC4( Key + IV )
IV is transmitted in plain text, and is only 24 bit long: repetitions are possible, thus allowing analysis
Once knowing the key, it is allowed Hub equivalent sniffing in promiscuous mode
Frames can be altered without knowing the key
ICV = CRC-32  lot of predictable collisions

## Slide 56: Wep Frame Format

## Slide 57: WEP Authentication (open)

## Slide 58: WEP Shared key authentication

## Slide 59: WEP weaknesses
IV space is 24 bit = 16M
Any IV can be reused at any time
  Allows replay attacks: one can collect lot of data encrypted with the IV of choice
Can decode RC4 sequence without knowledge of the key
Can find conflicting packets with same ICV

## Slide 60: WPA: TKIP encryption scheme

## Slide 61: WPA Personal
Pre-shared key with improvements
  TKIP: keeps RC4 with longer IVs: can’t be reused. The new MIC (Message Integrity Check) was more cryptographically robust
WPA2  CCMP = AES with special cipher mode
  Session PTK & GTK are exchanged during authentication. PTKs are Peer to Peer (WPA and WPA2)
Even if you know the pre-shared key, you can’t directly decode everybody’s else traffic
PTKs & GTKs are periodically re-generated

## Slide 63: Key hierarchy

## Slide 64: WPA Authorization process
PTK
PRF-X: RfC 4346

## Slide 65: WPA-Personal
Step 2 is not present in WPA1/2-Personal
MK is obtained directly from PMK
PMK (256 bit) is obtained from passphrases according to a fixed algorithm
  PBKDF2 (P, S, c, dkLen) = PMK (see RfC 2898)
where:
  PBKDF2 is a HMAC-SHA1 «repeated» c times over P and S
  P = passphrase, S = SSID, c = 4096 (!)
  Output: PMK, (dkLen =256 bit long)
Possibility of rainbow table attack over common SSID
  Rainbow tables: http://www.renderlab.net/projects/WPA-tables/
  Bruteforcer: coWPAtty
  Rainbow table generator : Pyrit
  Most common SSIDs: http://www.wigle.net/gps/gps//Stat
Commond SSID should be avoided… as well as common passwords, but this is another story.

## Slide 66: WPA Enterprise
An authenticated server comes into play
Personal account are now possible. There is no MASTER PMK

## Slide 67: 802.1x Authentication steps

## Slide 68: Step 1: pre-auth

## Slide 69: Step 2: Authentication
Step 3: Normal 4-way but with MK

## Slide 70: Role of the RADIUS server
Provides AAA services
  Authentication
  Authorization
  Accounting
Talks only with authorized authenticators providing the right “RADIUS secret”
(Authenticator == Access Point)

## Slide 71: Proof of concept: the Eduroam network

## Slide 72: PROs and CONs of a WPAx-Enterprise
Can handle individual accounts
  Better accountability, personal firewalling, etc.
More robust authentication on the AP+RADIUS side
Need more resources and careful configuration
RADIUS certificates still poorly handled on client side

## Slide 73: CVE-2012-4366
Generation of passphrase based on the AP MAC value for some Belkin AP models.
Example of CWE-656
  Reliance on security through obscurity
On many old Telecom routers, the default WPA passphrase could be generated from router’s MAC address using an hardwired «encryption» algorithm

## Slide 74: Other Things to know
WPA-Personal does not ensure PFS (Perfect Forward Secrecy)
De-Authentication  DoS
Rogue APs
  Localization?
WPA2-Enterprise can sometimes be worse than WPA2-Personal
WPS: quick association, but known to be WEAK
Why ARP Spoofing is still possible?

## Slide 75: WPA3
New handshake type: pfs, no rainbow tables
  WPA3-SAE (dragonfly handshake, RFC7664)
P2P encryption on open wifi-s
  Wifi enhanced open (OWE Opportunistic Wifi Encryption)
New encryption modes
Protected management frames

## Slide 77: Summary: Wired & Wireless
MITM attacks
  MAC Spoofing, port stealing (Wired, and sometimes Wireless open+wep)
  ARP  IP Spoofing (All)
  DHCP Spoofing (All)
  Broadcast attacks (All)
Wireless
  Open WLANs, WEP WLANs : virtually an Ethernet domain with an hub
  WPA & WPA2 WLANs: private unicast, possibility of user isolation