## Slide 1
Network Security Laboratory Session 6
Layer 3 attacks

## Slide 2
IP Spoofing
Similar to ARP spoofing attack but it relies on the IP address of a victim host
There are many different techniques to perform this attack but the most common is to use an ARP poisoner
In this case the ARP poisoner will send ARP reply associating our MAC address to the victim IP Address
When the router will forward packets the attacker will receive all the data

## Slide 3
Man In The Middle (MITM)
All the attacks we built so far are part of MITM
A MITM is a type of attack in which an Host is able to capture, read and forward packets of other hosts
We will try to create a full-duplex MITM, based on ARP Spoofing, using ettercap

## Slide 4
Ettercap
Ettercap is a well-known tool for MITM attacks
We will focus on ARP spoofing
Install Ettercap using the following command:
    sudo apt install ettercap-text-only

## Slide 5
DHCP Spoofing
DHCP Spoofing attack is the most relyable MITM attack
A victim will receive an IP address from the Rogue DHCP server and will be connected to its subnet
All traffick will be captured from the Rogue server

## Slide 6
DHCP Spoofing